## Slide 1
AeroMind
Prototype evidence: what the working system does, and what we measured
Project FY27-605244 · Tata InnoVent 2027 · AI at the Edge Solutions for Aerospace
Every number in this section is regenerated by `python -m aeromind report`. Aircraft data is simulated unless marked REAL DATA.

## Slide 2
One second of sensor data in, one decision out
Runs on the aircraft for every 1-second window; only the advisory is downlinked
Sensor health
stuck, drift, spikes,
dropout, range
›
Fusion
21 features incl.
OAT and altitude
›
Anomaly score
Isolation Forest
+ autoencoder
›
Persistence gate
5 of 8 windows
›
Fault class
gradient-boosted trees
on context residuals
›
RUL + interval
p10 / p50 / p90,
conformal
›
Evidence + ACARS
bearing defect
frequencies, ≤220 chars
On the ground
Decision engine
P(failure before next check) → ground now / replace at next check / defer
Work order
task, part, window, evidence and the ACARS text
Fleet ROI
reactive vs fixed-interval vs AeroMind, with a sensitivity range
Signed OTA
Ed25519 + SHA-256; tampered models rejected, rollback

## Slide 3
Measured, not promised
Headline results from the prototype
REAL DATA · NASA IMS
74.8 h
warning before a real bearing's outer-race failure
SIMULATED
0.0%
anomaly gate open on healthy flights (98.6% without flight-phase awareness)
SIMULATED
0
false component alarms from 7 kinds of injected sensor failure
SIMULATED
5/6
oil contamination correct at first classification under flight phases
SIMULATED
141/220
characters: every advisory fits one ACARS downlink block
CPU, NOT JETSON
1.2 ms
per window on one CPU thread; 1.8 MB of models

## Slide 4
On real data, it sees the failure coming
Left: NASA IMS bearing run-to-failure (REAL). Right: NASA C-MAPSS turbofan RUL benchmark
Chart: Outer-race signature (BPFO envelope SNR) vs test hour
Chart: RUL error, RMSE in cycles (lower is better)
| FD001 | FD002 | FD003 | FD004
AeroMind LSTM | 16.003 | 14.645 | 16.11 | 15.781
AeroMind trees | 19.377 | 17.745 | 22.255 | 20.1
Constant baseline | 48.5 | 52.4 | 62.9 | 61.9
IMS: alarm and BPFO evidence 74.8 h before the end of the test; bearing 1 has the strongest signature in 98.9% of snapshots once it appears. C-MAPSS: official test split, 3 seeds; C-MAPSS engines are simulated by NASA.

## Slide 5
Live demo: break the aircraft, watch it respond
python -m aeromind serve · six simulated aircraft · works offline
1
Inject bearing wear: score rises, gate opens, fault named, RUL falls, physics evidence, decision, work order, ACARS
2
Fail a temperature sensor: SENSOR_FAULT, channel masked, no false gearbox alarm
3
Push a signed model: accepted. Push a tampered one: rejected, fleet stays on the last valid model
4
Drag the what-if slider: the decision changes with the time to the next check

## Slide 6
The business case holds under harsh assumptions
Maintenance cost vs reactive, 30 aircraft × 3,000 flight hours (simulation)
Chart: Cost saving vs reactive maintenance (%)
| As measured | Weak detection, short warning | AOG $10k/h | All harsh
AeroMind | 98.6 | 60.4 | 84.2 | 34.4
Fixed interval | 24 | 24 | -10.4 | -10.4
Reactive: 44 unscheduled removals, 528 AOG hours
AeroMind as measured: 0 unscheduled, 0 AOG hours, 44 parts (fixed interval: 122)
Harsh case: 67% detection, 10% of the warning time, 5 false advisories per 1,000 windows, AOG at $10k/h
Detection and warning times are measured; costs and failure rates are labelled assumptions

## Slide 7
The fleet learns together, without sharing raw data
Each aircraft has seen only 2 of 5 fault types; models share weights only (federated averaging)
Chart: Classification accuracy (%), mean of 3 seeds
| Fault types seen locally | Fault types never seen locally
Local only | 99.6 | 0
Federated | 92.3 | 91.3
Pooled raw data (upper bound) | 100 | 100
Secure model updates
Model packages signed with Ed25519
Every model file pinned by SHA-256 in the signed manifest
Tampered package rejected before install; fleet keeps the last valid model
One-click rollback to the previous version

## Slide 8
What is not proven yet, and what comes next
Limits
No flight data: the fleet is simulated; real-data evidence is one bearing rig (IMS) and NASA's simulated engines (C-MAPSS)
Not yet run on a Jetson or TensorRT; timings are CPU
No certification work; decisions follow a configurable prototype policy
Costs and failure rates in the ROI model are assumptions
Next
Jetson build and power/latency measurement (kit ready)
Real multi-sensor data with an operator or MRO partner
Hardware-in-the-loop bench with a vibration sensor
Integration pilot with an MRO work-order system